## Thir_009
Accumulation phase
1. 2x2 sources --> 10secs
2. 1,3,4 sources scan at consistent start density
3. Add 5, 7, 9e19 line int density start points
4. LBO injection into peaked phase

For #1, wants S3+S7, switch to S4+S8 after 5s, but then each box has to run 10s. Maybe better to do each box at a time. Is then difficult for impurity densities though – talk to Paul.

## Thir_015
Scan ECRH reintroduction time

## ygao_009
Power/density steps for power exhaust
Wants no change in Itor… how?
ECCD?
He has this in other configs, is there someone’s we can copy, or am I the first?
P_ECRH = 3,5,7 MW, ne = 4,6,8e19
Can we do this pre- or post-NBI?
Post-NBI might be lower Itor.
Why in separate discharges?
## Daz_020
Modify profiles with gas puff during NBI peaking.
Scan ne=2 to 9e19 at switch to NBI
## dacar_011
Requires pure NBI ramp. Covered by all of thir_009, 015, …

## dmmo_029
Wants ‘constant plasma conditions’ with NBI?
Ask what he can do with the NBI discharges as is, only one or two (if any) will have ~ const in ECRH+NBI phase.
## Shas_005
For HPP.
Wants reintroduction shot, with modulated S4.
Can we do 1.5 source part of source scan, with e.g. S8+S4 modulated.
Continue through to ECRH reintro phase.
## Sban_002
Do 10s pure NBI, starting at ne=4e19 (HST!!!) and wait to see if it transitions.
Given that #230214.041 didn’t do anything, this will probably do nothing other than cook the beam dump tiles. Maybe use this with gas puff kick at e.g. 4s and cover daz_020?
## Dih_016
Move ICRH antenna in and see what NBI does to it.
This says it requires ‘short’ NBI pulses, which is incompatible with all the other programs. Can they accept long ones?
## gawe_040
Wants various modulation frequencies of reintroduces O2.
## Jproll_003
Wants high density gradients in high-mirror to compare to other configs. Should be entirely covered by extremes of thir_009. Not sure what she wants to measure. PCI, DR maybe?
## astechow_024
Wants highest possible densities. Covered by extremes of thir_009